## Slide 1
Inspiratory Arm
Expiratory Arm
Ventilator
Inspiratory Splitter Box
Expiratory Splitter Box
A
B
Filter
Filter
Patient A Tubing
Patient B Tubing
A
B
Filter
Filter
Patient A Tubing
Patient B Tubing
The goal of this design is to compartmentalize patient tubing so that patients can be added and removed without affecting other patients on the circuit. Thus, all components need to be separated by filters, but self-contained so clinicians aren’t having to attach individual splitter components. Flow control can initially be by a hand-controlled valve. #project-4-way-ventilator, Helpful Engineering (rev v4 7 April 2020)
Flow Meter
Flow Ctrl
PEEP Valve
Flow Meter
PEEP Valve
Splitter
Splitter
1-way
Valve
1-way
Valve
Flow Control
Flow Control
Flow Ctrl